## Slide 1
Scientific Roadmap towards Height System Unification with GOCE
5th International GOCE User Workshop, Paris, 27.11.2014
Th. Gruber(1), R. Rummel(1), M. Sideris(2), E. Rangelova(2), P. Woodworth(3),
C. Hughes(3), J. Ihde(4), G. Liebsch(4), A. Rülke(4), Ch. Gerlach(5),
R. Haagmans(6)
(1) Institute for Astronomical and Physical Geodesy, Technical University Munich, Germany
(2) Department of Geomatics Engineering, University of Calgary, Canada
(3) National Oceanography Centre, Liverpool, United Kingdom
(4) Bundesamt für Kartographie und Geodäsie (BKG), Frankfurt/Main, Germany
(5) Kommission für Erdmessung und Glaziologie, Bayerische Akademie der Wissenschaften, Munich Germany
(6) European Space Agency, The European Space Research and Technology Centre, Noordwijk, The Netherlands
ESA Project:
Support to Science Element (STSE) GOCE+ Theme 1: Height System Unification (HSU)

## Slide 2
Outline
Upper-Rhine Bridge; Germany – Switzerland:
27 cm height offset applied with wrong sign
Problem Overview
Essential Tasks (Scientific Roadmap)
  Diagnosis of Height Systems
  Global Height System Unification
  Ocean Levelling
  GNSS/Levelling in well surveyed Land Areas
  GNSS/Levelling in sparsely surveyed Land Areas
Conclusions

## Slide 3
GOCE Equipotential Surface (long wavelengths)
Local Vertical Datum (Equipotential Surface)
Local Physical Height
True Equipotential Surface (short wavelengths)
Local Geoid Height
GOCE Physical Height
Omission Error
Problem Overview
Vertical Datum A
Vertical Datum C
A
C
B
Vertical Datum B
GPS Benchmarks
Tide Gauge Benchmark
Levelling Network
GOCE Geoid Height

## Slide 4
Scientific Roadmap – Essential Tasks
The geopotential and geoid improvements resulting from GOCE are the basis of a reassessment of global height systems
Diagnosis of existing height systems by comparison with GOCE geoid

## Slide 5
Scientific Roadmap – Diagnosis of Height Systems
Diagnosis of existing Height Systems by Comparison of GPS/Levelling with GOCE Geoid
Reference:
Long-wavelength errors of the US vertical datum (Wang et al., 2012)
Australian GPS/Levelling vs. GOCE-TIM5 Geoid
US GPS/Levelling vs. GOCE-TIM5 Geoid
Canadian GPS/Levelling vs. GOCE-TIM5 Geoid

## Slide 6
Scientific Roadmap – Diagnosis of Height Systems
Diagnosis of existing Height Systems by Comparison of GPS/Levelling with GOCE-TIM5 Geoid for some European Countries
France
UK
Germany
Italy
Netherlands
40 cm
30 cm
25 cm
40 cm
5 cm

## Slide 7
GOCE Equipotential Surface (long wavelengths)
Vertical Datum A
Vertical Datum C
A
C
B
Vertical Datum B
GPS Benchmarks
Tide Gauge Benchmark
Levelling Network
Regional Height Reference Surface (Geoid?)
Scientific Roadmap – Diagnosis of Height Systems
GOCE Physical Height
Regional Height

## Slide 8
Scientific Roadmap – Diagnosis of Height Systems
Diagnosis of existing Height Systems by Comparison of GPS/Levelling with GOCE-TIM5
- before and after subtracting a regional Correction Surface
GPS-Lev. Geoid Differences
Correction Surface
Residual Differences
What causes these systematic differences: GOCE geoid, Levelling or GPS Heights?
GOCE geoid error is below 2 cm globally – cannot be the reason.
Levelling is sensitive to systematic distortions – most likely the main reason.
Observation GPS height error 1-2 cm randomly distributed – cannot be the reason.
But what about the coordinate frames?

## Slide 9
Scientific Roadmap – Diagnosis of Height Systems
Impact of Coordinate Frame Transformations on GPS Heights
(Study performed by G. Liebsch, BKG)
GPS and geoid heights need to be in a consistent frame.
GOCE geoid heights refer to CoM.
GPS heights refer to an ITRFxxxx with a center of origin which is not consistent to CoM.
ITRF2008 is known to be close to CoM.
ITRF1989 (ETRF1989) to ITRF2008 offset is (x,y,z): 2.8 - 3.9 - 10.1 cm
7 parameter Helmert transformation (plus linear trends) result in height change of up to 7 cm in Europe (see figure).
When GPS and GOCE geoid heights are jointly used in GPS-Levelling this needs to be taken into account.

## Slide 10
Scientific Roadmap – Essential Tasks
The geopotential and geoid improvements resulting from GOCE are the basis of a reassessment of global height systems
Realization of a globally unified height system but confined to a global set of primary stations (national datum points, fundamental stations, primary tide gauges, primary clocks).
Global Height System Unification
Diagnosis of existing height systems by comparison with GOCE geoid (100 km)

## Slide 11
Scientific Roadmap – Global Height System Unification
Observed Geoid Height referring to vertical Datum A
Geoid Height Offset of vertical Datum A wrt. “mean” Geoid.
Geoid height from GOCE model
Residual geoid height (omission)
Observation Equation
from spirit levelling referring to height datum A (e.g. tide gauge)
from GNSS positioning referring to a specific ellipsoid
Computed Geoid Height referring to “mean” Geoid
Geoid
Height System Offset wrt. Geoid

## Slide 12
Scientific Roadmap – Global Height System Unification
per degree
from degree (to infinity)
Omission error can be estimated from EGM2008 and/or residual terrain modelling
Omission Error

## Slide 13
Scientific Roadmap – Global Height System Unification
GOCE –TIM5 Model truncated at D/O 200

## Slide 14
Scientific Roadmap – Global Height System Unification
GOCE
Geoid
Australia
(Mainland)
-101
England
-34
Germany
-3
-115
USA
(1999)
USA
(2009)
-11
Greece
-72
Japan
-2
Canada
-59
Brazil
+67
-81
+14
GOCE-TIM5 (0-200) &
EGM2008 (201-2190)
+4
GOCE
Geoid
Australia
(Mainland)
-97
England
-34
Germany
+3
-111
USA
(1999)
USA
(2009)
-15
Greece
-67
Japan
+11
Canada
-52
Brazil
+63
-77
+14
+4
GOCE-TIM5 (0-200)
Results from Rapp (1994) (Bulletin Geodesique 69, p.26-31) based on JGM-2 / OSU91A and Geoid Heights on Doppler Stations.
-76
+4
+72

## Slide 15
Scientific Roadmap – Essential Tasks
The geopotential and geoid improvements resulting from GOCE are the basis of a reassessment of global height systems
Realization of a globally unified height system but confined to a global set of primary stations (national datum points, fundamental stations, primary tide gauges, primary clocks).
Open Oceans and Coastal Zones
Global Height System Unification
Diagnosis of existing height systems by comparison with GOCE geoid (100 km)
Realization of a globally consistent model of mean dynamic ocean topography at tide gauges and at sea (Ocean Levelling).

## Slide 16
Scientific Roadmap – Ocean Levelling
Sea level slope at tide gauges along the east coast of North America from
classical geodetic leveling (top: USA in red, Canada in blue),
from an ocean circulation model (black) and
from GNSS-Levelling based on GOCE DIR5 & EGM2008 (bottom: red & blue)
(Study performed by Phil Woodworth, NOC)

## Slide 17
Scientific Roadmap – Essential Tasks
The geopotential and geoid improvements resulting from GOCE are the basis of a reassessment of global height systems
Realization of a globally unified height system but confined to a global set of primary stations (national datum points, fundamental stations, primary tide gauges, primary clocks).
Open Oceans and Coastal Zones
Global Height System Unification
Well Surveyed Areas (Land)
Diagnosis of existing height systems by comparison with GOCE geoid (100 km)
Realization of a globally consistent model of mean dynamic ocean topography at tide gauges and at sea.
Regional geoid based on GOCE model. Establishment of national or regional height systems at primary points (first and second order) based on the technique of “GNSS-leveling”.

## Slide 18
Scientific Roadmap – Well Surveyed Areas
GOCE Equipotential Surface (long wavelengths)
True Equipotential Surface (short wavelengths)
True Geoid Height
GNSS Receiver
GOCE Geoid Height
h
NGOCE
N
Assumptions:
Network of permanent, high quality GNSS stations. Observation of h
GOCE geopotential/geoid model. Determination of NGOCE
Regional gravity and topographic data.
Refined GOCE geoid model leading to a regional geoid. Determination of N
Consistent reference frames for h and NGOCE / N
H
H = h - N
H = h - NGOCE
Omission Error = N - NGOCE

## Slide 19
Mean Differences of GOCE TIM5 and GPS-Levelling Geoid Heights & Omission Error from EGM2008 from D/O 181 to 2190
with omission error (signal)
w/o omission error (signal)
-1.221
-3.729
+0.422
-0.840
Guam
+0.493
-0.605
Marianas
Samoa
Guam & Marianas
Scientific Roadmap – Well Surveyed Areas

## Slide 20
Scientific Roadmap – Essential Tasks
The geopotential and geoid improvements resulting from GOCE are the basis of a reassessment of global height systems
Realization of a globally unified height system but confined to a global set of primary stations (national datum points, fundamental stations, primary tide gauges, primary clocks).
Open Oceans and Coastal Zones
Global Height System Unification
Well Surveyed Areas (Land)
Sparsely Surveyed Areas (Land)
Diagnosis of existing height systems by comparison with GOCE geoid (100 km)
Realization of a globally consistent model of mean dynamic ocean topography at tide gauges and at sea.
Establishment of national or regional height systems at primary points (first and second order) based on the technique of “GNSS-leveling”.
Establishment of a master plan:
realization of datum point
first-order GNSS reference points
diagnosis of regional gravity and/or leveling and/or topographic data base

## Slide 21
Scientific Roadmap – Sparsely Surveyed Areas
Model Equipotential Surface
Model Geoid Height
GNSS Receiver
h
NModel
H
Height of Mount Everest:
h = 8821.47 m (average from GPS and classical techniques for snow surface)
(Chen, J. et al, 2006, Science in China; doi: 10.1007/s11430-006-0531-1
NGOCE = -26.58 m
NEGM = -22.90 m
(GOCE-TIM5 d/o 280)
(EGM2008 d/o 2190)
this leads to heights above sea level:
HGOCE = 8848.05 m
HEGM = 8844.37 m
Ellipsoidal Height
Height above Sea Level
Large uncertainty in omission error estimate due to lack of gravimetric data.
NGOCE/EGM = -22.19 m
(GOCE-TIM5 d/o 200 & EGM2008 d/o 201-2190)
Model geoid height for H=0
Model geoid height from height anomaly and correction terms (c.f. Rapp, 1997, JoG).
NEGM/Rapp = -28.50 m
(EGM2008 d/o 2190)
HEGM/Rapp = 8849.97 m
HChen = 8847.93 m (based on local geoid)

## Slide 22
Conclusions
The GOCE geoid represents a reference for global and regional height systems with unprecedented spatial resolution.
GOCE enables the diagnosis of systematic distortions in existing height systems.
GOCE enables global height system unification if the omission error at height reference stations can be quantified.
The GOCE geoid supports results obtained from ocean models at tide gauges.
GOCE supports GNSS/Levelling.
  In well surveyed areas a GOCE based regional geoid and consistent reference frames shall be used.
  In sparsely surveyed areas the GOCE geoid in many cases represents the best possible reference surface. Data for regional geoid modelling have to be acquired.

## Slide 23
Final Remark
Project results are available at the following web-site:
http://www.goceplushsu.eu